## Slide 1: Cutting laser maintenance procedures

## Slide 2: Things to be done daily
Check for Coolant Leak by checking the electronics compartment. Since the coolant is in a sealed system, a lower than usual coolant level may signify major complications

## Slide 3: Things to do weekly
Clean reflecting mirrors and the lens. There are 3 mirrors and 1 lens
Apply lubrication to the rails. There are 3 rails. Use 3 in 1 oil
Check for proper beam alignment

## Slide 4: Things to do quaterly
Tighten the belts if necessary. Do not over tension
Clean the rails. Basically apply lubrication and wipe it off before reapplying the lubrication
Check condition of water in the coolant reservoir and replace if necessary
Upload configurations file for the ‘Laser Cut’ software
Check back cabinet for dust and clean if necessary
Check for loose wires
Grease the leveler screws