## Slide 1: Stuff I brought back from Fermilab
20+ troughs for epoxing straws
13 straw clamps
5 CO2 readers
5 termination endpieces
4 barcode scanners
~1000 straws

## Slide 2
1.
Initial Storage
Load Pallet on Cart
Remove paper, Conductivity Test
Epoxy CO2 ends
Epoxy cure storage
Pressurize straws, Leak test
Laser Cut 1
Laser Cut 2
Detach Cut straws
Epoxy termination pieces
Cure epoxy
Termination Conductivity Test
Package for shipping
Tented
Suit Up Area
2.
3.
4.
5.
6.
7.
8.
9.
10.
11.
12.
13.

## Slide 3: To make this outline happen?
Needs:
Tables
Storage areas
Remove current work benches
Remove/store current equipment
Tape out room, make sure this fits

## Slide 4: Initial Storage
Receive large plastic tubes with ~1000 straws each
Storage ~5 feet long with another 5 ft to safely pull the straw directly out.
These can be built out of Unistrut for a solid clean and sturdy fixture.

## Slide 5: Straw Storage
Need 2 racks back to back to store 10 pallets
$65 a piece so $130 or $260 total
Loadable from either side
Centralized in room for ease of access
Replace bars for required distance
Remove wheels
Add
Safety
notches

## Slide 6: Leak Testing
We don’t want to have to tip the chambers to get the straws out.
Think of implementing a loop and hook at the end of plastic tubes.
Computer
Gas cylinders
Straw Prep Table

## Slide 7: Pallet loading, Conductivity Test
Large table
Put straws into pallet
Barcode scan straw batch and pallet
Remove paper
Test conductivity
Leaves room for storage til epoxy

## Slide 8: Pallets
Look at CAD drawings